Aaron Andal

UF3 - ADMINISTRACIÓ AVANÇADA DE XARXES
Activitat 2.2. Enrutament complex d'VLAN

Amb les següents VLAN:
● VLAN 1 - Nativa
● VLAN 50 - 172.24.50.0/24
● VLAN 60 - 172.24.60.0/24
● VLAN 100 (Administració) - 172.24.100.0/24
I la següent distribució entre VLAN, switchs i ports:
VLAN	Switch0	Switch1
1	fa0/1 i fa0/2	fa0/1
50	fa0/4 - fa0/10	fa0/2 - fa0/6
60	fa0/11 - fa0/24	fa0/7 - fa0/12
100	fa0/3	none

Digueu quines són les configuracions necessàries per tal que: tots els PC i el Server0 s'han de poder fer ping entre ells.

Als switch s’ha de configurar les vlan amb interfícies troncals(al S0 la fa0/1 i fa0/2 i al S1. / la fa0/1). / Al router s’ha de configurar les tres interfícies virtuals. / Switch0 / CONFIGURAR LES VLAN / Switch(config)#int range fa0/4-10 / Switch(config-if-range)#switchport mode access / Switch(config-if-range)#switchport access vlan 50 / % Access VLAN does not exist. Creating vlan 50 / Switch(config-if-range)#no shutdown / Switch(config-if-range)#exit / Switch(config)#int range fa0/11-24 / Switch(config-if-range)#switchport mode access / Switch(config-if-range)#switchport access vlan 60 / % Access VLAN does not exist. Creating vlan 60 / Switch(config-if-range)#exit / Switch(config)#int range fa0/11-24 / Switch(config-if-range)#no shutdown / Switch(config-if-range)#int fa0/3 / Switch(config-if)#int fa0/3 / Switch(config-if)#switchport mode access / Switch(config-if)#switchport access vlan 100 / % Access VLAN does not exist. Creating vlan 100 / Switch(config-if)#no shutdown / Switch(config-if)#exit / Switch(config)#int fa0/1 / Switch(config-if)#switchport mode trunk / Switch(config-if)#switchport trunk allowed vlan 50,60 / Switch(config-if)#no shutdown / Switch(config-if)#exit / Switch(config)#int fa0/2 / Switch(config-if)#switchport mode trunk / Switch(config-if)#switchport trunk allowed vlan 50,60,100 / Switch(config-if)#no shutdown / Switch(config-if)#exit / Switch1 / CONFIGURAR LES VLAN / Switch(config)#int range fa0/2-6 / Switch(config-if-range)#switchport access vlan 50 / % Access VLAN does not exist. Creating vlan 50 / Switch(config-if-range)#no shutdown / Switch(config-if-range)#exit / Switch(config)#int range fa0/7-12 / Switch(config-if-range)#switchport mode access / Switch(config-if-range)#switchport access vlan 60 / Switch(config-if-range)#exit / Router0 / CONFIGURAR LES INTERFÍCIES VIRTUALS I LES VLAN / Router(config)#int fa0/0.50 / Router(config-subif)#ip address 172.24.50.1 255.255.255.0 / Router(config-subif)#encapsulation dot1Q 50 / Router(config-subif)#exit / Router(config)#int fa0/0.60 / Router(config-subif)#ip address 172.24.60.1 255.255.255.0 / Router(config-subif)#encapsulation dot1Q 60 / Router(config-subif)#exit / Router(config)#int fa0/0.100 / Router(config-subif)#ip address 172.24.100.1 255.255.255.0 / Router(config-subif)#encapsulation dot1Q 100 / Router(config-subif)#exit / Comprovacions de connectivitat / PCAdmin / C:\>ping 172.24.60.3 / Pinging 172.24.60.3 with 32 bytes of data: / Reply from 172.24.60.3: bytes=32 time<1ms TTL=127 / Reply from 172.24.60.3: bytes=32 time=1ms TTL=127 / Reply from 172.24.60.3: bytes=32 time=1ms TTL=127 / Ping statistics for 172.24.60.3: / Packets: Sent = 3, Received = 3, Lost = 0 (0% loss), / Approximate round trip times in milli-seconds: / Minimum = 0ms, Maximum = 1ms, Average = 0ms / PC1 / C:\>ping 172.24.60.3 / Pinging 172.24.60.3 with 32 bytes of data: / Reply from 172.24.60.3: bytes=32 time<1ms TTL=127 / Reply from 172.24.60.3: bytes=32 time<1ms TTL=127 / Reply from 172.24.60.3: bytes=32 time=15ms TTL=127 / Reply from 172.24.60.3: bytes=32 time<1ms TTL=127 / Ping statistics for 172.24.60.3: / Packets: Sent = 4, Received = 4, Lost = 0 (0% loss), / Approximate round trip times in milli-seconds: / Minimum = 0ms, Maximum = 15ms, Average = 3ms / PC2 / C:\>ping 172.24.60.3 / Pinging 172.24.60.3 with 32 bytes of data: / Reply from 172.24.60.3: bytes=32 time<1ms TTL=128 / Reply from 172.24.60.3: bytes=32 time<1ms TTL=128 / Reply from 172.24.60.3: bytes=32 time<1ms TTL=128 / Reply from 172.24.60.3: bytes=32 time<1ms TTL=128 / Ping statistics for 172.24.60.3: / Packets: Sent = 4, Received = 4, Lost = 0 (0% loss), / Approximate round trip times in milli-seconds: / Minimum = 0ms, Maximum = 0ms, Average = 0ms / PC3 / C:\>ping 172.24.60.3 / Pinging 172.24.60.3 with 32 bytes of data: / Reply from 172.24.60.3: bytes=32 time<1ms TTL=127 / Reply from 172.24.60.3: bytes=32 time<1ms TTL=127 / Reply from 172.24.60.3: bytes=32 time<1ms TTL=127 / Reply from 172.24.60.3: bytes=32 time<1ms TTL=127 / Ping statistics for 172.24.60.3: / Packets: Sent = 4, Received = 4, Lost = 0 (0% loss), / Approximate round trip times in milli-seconds: / Minimum = 0ms, Maximum = 0ms, Average = 0ms / PC4 / C:\>ping 172.24.60.3 / Pinging 172.24.60.3 with 32 bytes of data: / Reply from 172.24.60.3: bytes=32 time=4ms TTL=128 / Reply from 172.24.60.3: bytes=32 time<1ms TTL=128 / Reply from 172.24.60.3: bytes=32 time=5ms TTL=128 / Reply from 172.24.60.3: bytes=32 time=5ms TTL=128 / Ping statistics for 172.24.60.3: / Packets: Sent = 4, Received = 4, Lost = 0 (0% loss), / Approximate round trip times in milli-seconds: / Minimum = 0ms, Maximum = 5ms, Average = 3ms