Aaron Andal
17.04.22- M07 Xarxes
## Activitat 2.3. Enrutament complex

Una taula resum de les adreces IP assignades a cada interfície de cadascun dels routers (Router / Interfície / Adreça IP)

Dispositiu	Interfície	Adreça IP
PC 0	FastEthernet0	10.0.0.2/16
R0	FastEthernet0/0	10.0.0.1/16
	FastEthernet1/0	10.1.0.1/16
	FastEthernet5/0	192.168.1.1/30
	FastEthernet4/0	192.168.0.5/30
PC 1	FastEthernet0	10.1.0.2/16
R1	FastEthernet0/0	10.2.0.1/16
	FastEthernet4/0	192.168.1.2/30
	FastEthernet5/0
	Serial0/2/0	192.168.0.9/30
PC 2	FastEthernet0	10.2.0.2/16
R2	FastEthernet0/0	10.4.0.1/16
	FastEthernet1/0	10.5.0.1/16
	FastEthernet4/0	192.168.0.6/30
	FastEthernet5/0
PC 3	FastEthernet0	10.0.0.2/16
R3	FastEthernet0/0	10.3.0.2/16
	Serial0/3/0 (Cloud)
	Serial0/2/0	192.168.0.10/30
PC 4	FastEthernet0	10.4.0.2/16
PC 5	FastEthernet0	10.5.0.2/16

Una taula resum de les taules d’enrutament de cadascun dels routers (Router / AX / MX / IPHOP)

Routing estátic / La pregunta és la mateixa: / Per anar a la Xarxa X hem de pasar per la Interfície Serial X. S’ha de fer també la tornada. Es crea un Túnel VPN.

Router	Per anar a la AX	Amb MX	Surts per IPHop
R0	10.2.0.0/16	255.255.0.0	192.168.1.2
	10.3.0.0/16	255.255.0.0	192.168.1.2
	10.4.0.0/16	255.255.0.0	192.168.0.6
	10.5.0.0/16	255.255.0.0	192.168.0.6
R1	10.1.0.0/16	255.255.0.0	192.168.1.1
	10.0.0.0/16	255.255.0.0	192.168.1.1
	10.4.0.0/16	255.255.0.0	192.168.1.1
	10.5.0.0/16	255.255.0.0	192.168.1.1
	10.3.0.0/16	255.255.0.0	192.168.0.10
R2	10.0.0.0/16	255.255.0.0	192.168.0.5
	10.1.0.0/16	255.255.0.0	192.168.0.5
	10.2.0.0/16	255.255.0.0	192.168.0.5
	10.3.0.0/16	255.255.0.0	192.168.0.5
R3	10.5.0.0/16	255.255.0.0	192.168.0.9
	10.4.0.0/16	255.255.0.0	192.168.0.9
	10.0.0.0/16	255.255.0.0	192.168.0.9
	10.1.0.0/16	255.255.0.0	192.168.0.9
	10.2.0.0/16	255.255.0.0	192.168.0.9

R0:
R0(config)#ip route 10.2.0.0 255.255.0.0 192.168.1.2
R0(config)#ip route 10.3.0.0 255.255.0.0 192.168.1.2
R0(config)#ip route 10.4.0.0 255.255.0.0 192.168.0.6
R0(config)#ip route 10.5.0.0 255.255.0.0 192.168.0.6

R1:
R1(config)#ip route 10.1.0.0 255.255.0.0 192.168.1.1
R1(config)#ip route 10.0.0.0 255.255.0.0 192.168.1.1
R1(config)#ip route 10.4.0.0 255.255.0.0 192.168.1.1
R1(config)#ip route 10.5.0.0 255.255.0.0 192.168.1.1
R1(config)#ip route 10.3.0.0 255.255.0.0 192.168.0.10

R2:
R2(config)#ip route 10.0.0.0 255.255.0.0 192.168.0.5
R2(config)#ip route 10.1.0.0 255.255.0.0 192.168.0.5
R2(config)#ip route 10.2.0.0 255.255.0.0 192.168.0.5
R2(config)#ip route 10.3.0.0 255.255.0.0 192.168.0.5

R3:
Router(config)#ip route 10.5.0.0 255.255.0.0 192.168.0.9
Router(config)#ip route 10.4.0.0 255.255.0.0 192.168.0.9
Router(config)#ip route 10.0.0.0 255.255.0.0 192.168.0.9
Router(config)#ip route 10.1.0.0 255.255.0.0 192.168.0.9
Router(config)#ip route 10.2.0.0 255.255.0.0 192.168.0.9

Les comandes utilitzades per a configurar els routers

PC0 a la PC5: Com no tenim DHCP les configurem manualment les IP (Segons la taula definida abans) I li posem el GATEWAY corresponent (Segons la taula definida abans). / R0: / R0>enable / R0# / R0#configure terminal / Enter configuration commands, one per line. End with CNTL/Z. / R0(config)#interface FastEthernet0/0 / R0(config-if)#ip address 10.0.0.1 255.255.0.0 / R0(config-if)#no shutdown / R0(config-if)# / %LINK-5-CHANGED: Interface FastEthernet0/0, changed state to up / %LINEPROTO-5-UPDOWN: Line protocol on Interface FastEthernet0/0, changed state to up / R0(config-if)#exit / R0(config)#interface FastEthernet1/0 / R0(config-if)#ip address 10.1.0.1 255.255.0.0 / R0(config-if)#no shutdown / R0(config-if)# / %LINK-5-CHANGED: Interface FastEthernet1/0, changed state to up / %LINEPROTO-5-UPDOWN: Line protocol on Interface FastEthernet1/0, changed state to up / R0(config-if)#end / R0#copy running-config startup-config / Destination filename [startup-config]? / Building configuration... / [OK] / R0# / %SYS-5-CONFIG_I: Configured from console by console / R0# / R0#configure terminal / Enter configuration commands, one per line. End with CNTL/Z. / R0(config)#interface FastEthernet5/0 / R0(config-if)#ip address 192.168.1.1 255.255.255.252 / R0(config-if)#no shutdown / R0(config-if)# / R0(config-if)#exit / R0(config)#interface FastEthernet4/0 / R0(config-if)#ip address 192.168.0.5 255.255.255.252 / R0(config-if)#no shutdown / R0(config-if)# / %LINK-5-CHANGED: Interface FastEthernet4/0, changed state to up / %LINEPROTO-5-UPDOWN: Line protocol on Interface FastEthernet4/0, changed state to up / R0(config-if)#end / R0#copy running-config startup-config / Destination filename [startup-config]? / Building configuration... / [OK] / R0# / %SYS-5-CONFIG_I: Configured from console by console / R2 / R2>enable / R2#conf / R2#configure ter / R2#configure terminal / Enter configuration commands, one per line. End with CNTL/Z. / R2(config)#inter / R2(config)#interface Fa / R2(config)#interface FastEthernet 0/0 / R2(config-if)#ip address 10.4.0.1 255.255.0.0 / R2(config-if)#no shutdown / R2(config-if)# / %LINK-5-CHANGED: Interface FastEthernet0/0, changed state to up / %LINEPROTO-5-UPDOWN: Line protocol on Interface FastEthernet0/0, changed state to up / exit / R2(config)#interface Fa1/0 / R2(config-if)#ip address 10.5.0.1 255.255.0.0 / R2(config-if)#no shutdown / R2(config-if)# / %LINK-5-CHANGED: Interface FastEthernet1/0, changed state to up / %LINEPROTO-5-UPDOWN: Line protocol on Interface FastEthernet1/0, changed state to up / R2(config-if)#end / R2# / %SYS-5-CONFIG_I: Configured from console by console / R2#copy running-conf / R2#copy running-config start / R2#copy running-config startup-config / Destination filename [startup-config]? / Building configuration... / [OK] / R2# / R2# / R2#configure terminal / Enter configuration commands, one per line. End with CNTL/Z. / R2(config)#interface FastEthernet4/0 / R2(config-if)#ip address 192.168.0.6 255.255.255.252 / R2(config-if)#no shutdown / R2(config-if)# / %LINK-5-CHANGED: Interface FastEthernet4/0, changed state to up / %LINEPROTO-5-UPDOWN: Line protocol on Interface FastEthernet4/0, changed state to up / R2#copy running-conf / R2#copy running-config start / R2#copy running-config startup-config / Destination filename [startup-config]? / Building configuration... / [OK] / R2# / R1: / R1>enable / R1# / R1#configure terminal / Enter configuration commands, one per line. End with CNTL/Z. / R1(config)#interface FastEthernet0/0 / R1(config-if)#ip address 10.2.0.1 255.255.0.0 / R1(config-if)#no shutdown / R1(config-if)# / %LINK-5-CHANGED: Interface FastEthernet0/0, changed state to up / %LINEPROTO-5-UPDOWN: Line protocol on Interface FastEthernet0/0, changed state to up / R1(config-if)#exit / R1(config)#interface FastEthernet4/0 / R1(config-if)#ip address 192.168.1.2 255.255.255.252 / R1(config-if)#no shutdown / R1(config-if)# / %LINK-5-CHANGED: Interface FastEthernet4/0, changed state to up / %LINEPROTO-5-UPDOWN: Line protocol on Interface FastEthernet4/0, changed state to up / R1(config-if)#exit / R1(config)#interface Serial2/0 / R1(config-if)#ip address 192.168.0.9 255.255.255.252 / R1(config-if)#no shutdown / R1(config-if)# / R3: / Router>enable / Router# / Router#configure terminal / Enter configuration commands, one per line. End with CNTL/Z. / Router(config)#interface FastEthernet0/0 / Router(config-if)#ip address 10.3.0.1 255.255.0.0 / Router(config-if)#no shutdown / Router(config-if)# / %LINK-5-CHANGED: Interface FastEthernet0/0, changed state to up / %LINEPROTO-5-UPDOWN: Line protocol on Interface FastEthernet0/0, changed state to up / Router(config-if)# / Router(config-if)#exit / Router(config)#interface Serial2/0 / Router(config-if)#ip address 192.168.0.10 255.255.255.252 / Router(config-if)#no shutdown / Router(config-if)# / %LINK-5-CHANGED: Interface Serial2/0, changed state to up / Router(config-if)#end / Router#copy running-config startup-config / Destination filename [startup-config]? / Building configuration... / [OK] / Router# / %SYS-5-CONFIG_I: Configured from console by console / %LINEPROTO-5-UPDOWN: Line protocol on Interface Serial2/0, changed state to up

4. Les comandes utilitzades per comprovar la connectivitat correcta de tota la xarxa / a) Un ping del PC3 al PC5 / Cisco Packet Tracer PC Command Line 1.0 / C:\>ping 10.5.0.2 / Pinging 10.5.0.2 with 32 bytes of data: / Request timed out. / Request timed out. / Request timed out. / Reply from 10.5.0.2: bytes=32 time=4ms TTL=124 / Ping statistics for 10.5.0.2: / Packets: Sent = 4, Received = 1, Lost = 3 (75% loss), / Approximate round trip times in milli-seconds: / Minimum = 4ms, Maximum = 4ms, Average = 4ms / C:\>ping 10.5.0.2 / Pinging 10.5.0.2 with 32 bytes of data: / Reply from 10.5.0.2: bytes=32 time=9ms TTL=124 / Reply from 10.5.0.2: bytes=32 time=23ms TTL=124 / Reply from 10.5.0.2: bytes=32 time=6ms TTL=124 / Reply from 10.5.0.2: bytes=32 time=4ms TTL=124 / Ping statistics for 10.5.0.2: / Packets: Sent = 4, Received = 4, Lost = 0 (0% loss), / Approximate round trip times in milli-seconds: / Minimum = 4ms, Maximum = 23ms, Average = 10ms / C:\> / b) Un traceroute I ping del PC3 al PC0 / C:\>tracert 10.0.0.2 / Tracing route to 10.0.0.2 over a maximum of 30 hops: / 1 0 ms 0 ms 0 ms 10.3.0.1 / 2 0 ms 7 ms 0 ms 192.168.0.9 / 3 0 ms 13 ms 9 ms 192.168.1.1 / 4 * 2 ms 0 ms 10.0.0.2 / Trace complete. / C:\> / C:\>ping 10.0.0.2 / Pinging 10.0.0.2 with 32 bytes of data: / Reply from 10.0.0.2: bytes=32 time=7ms TTL=125 / Reply from 10.0.0.2: bytes=32 time=10ms TTL=125 / Reply from 10.0.0.2: bytes=32 time=4ms TTL=125 / Reply from 10.0.0.2: bytes=32 time=4ms TTL=125 / Ping statistics for 10.0.0.2: / Packets: Sent = 4, Received = 4, Lost = 0 (0% loss), / Approximate round trip times in milli-seconds: / Minimum = 4ms, Maximum = 10ms, Average = 6ms / C:\> / b) Un traceroute I ping del PC5 al PC2 / Cisco Packet Tracer PC Command Line 1.0 / C:\>ping 10.2.0.2 / Pinging 10.2.0.2 with 32 bytes of data: / Request timed out. / Reply from 10.2.0.2: bytes=32 time<1ms TTL=125 / Reply from 10.2.0.2: bytes=32 time<1ms TTL=125 / Reply from 10.2.0.2: bytes=32 time<1ms TTL=125 / Ping statistics for 10.2.0.2: / Packets: Sent = 4, Received = 3, Lost = 1 (25% loss), / Approximate round trip times in milli-seconds: / Minimum = 0ms, Maximum = 0ms, Average = 0ms / C:\>tracert 10.2.0.2 / Tracing route to 10.2.0.2 over a maximum of 30 hops: / 1 0 ms 0 ms 0 ms 10.5.0.1 / 2 0 ms 0 ms 0 ms 192.168.0.5 / 3 0 ms 0 ms 0 ms 192.168.1.2 / 4 0 ms 0 ms 0 ms 10.2.0.2 / Trace complete. / C:\>