Configureu amb el Packet Tracer la següent xarxa, utilitzant enrutament dinàmic:

Atenció! Errata: 163.27.176/20 (xarxa del PC0)
Per fer-ho, tingueu en compte els següents requisits:
Configureu els tres routers 1841 per tal que puguin tenir dos ports serial

Configureu les interfícies de cada router
Dispositiu	Interface	Direcció IP / Mascara
Router 0	FastEthernet 0/0	163.27.180.1 / 255.255.240.0
Router 0	FastEthernet 0/1	163.27.240.1 / 255.255.240.0
Router 0	Serial 0/0/0	192.168.2.1 / 255.255.255.252
Router>enable / Router#conf / Router#configure ter / Router#configure terminal / Enter configuration commands, one per line. End with CNTL/Z. / Router(config)#inter / Router(config)#interface Fa / Router(config)#interface FastEthernet 0/0 / Router(config-if)#ip address 163.27.180.1 255.255.240.0 / Router(config-if)#no shutdown / %LINK-5-CHANGED: Interface FastEthernet0/0, changed state to up / %LINEPROTO-5-UPDOWN: Line protocol on Interface FastEthernet0/0, changed state to up / Router(config-if)#exit / Router(config)#inter / Router(config)#interface Fa / Router(config)#interface FastEthernet 0/1 / Router(config-if)#ip address 163.27.240.1 255.255.240.0 / Router(config-if)#no shutdown / Router(config-if)# / %LINK-5-CHANGED: Interface FastEthernet0/1, changed state to up / %LINEPROTO-5-UPDOWN: Line protocol on Interface FastEthernet0/1, changed state to up / Router(config)#interface Serial 0/0/0 / Router(config-if)#ip address 192.168.2.1 255.255.255.252 / Router(config-if)#no shutdown / Router(config-if)#clock rate 19200 / %LINK-5-CHANGED: Interface Serial0/0/0, changed state to up / %LINEPROTO-5-UPDOWN: Line protocol on Interface Serial0/0/0, changed state to up
Router 1	FastEthernet 0/0	11.192.0.1 / 255.192.0.0
Router 1	FastEthernet 0/1	11.128.0.1 / 255.192.0
Router 1	Serial 0/0/0	192.168.2.2 / 255.255.255.252
Router 1	Serial 0/0/0	192.168.1.2 / 255.255.255.252
Router>enable / Router#configure terminal / Enter configuration commands, one per line. End with CNTL/Z. / Router(config)#interface Fa / Router(config)#interface FastEthernet 0/0 / Router(config-if)#ip address 11.192.0.1 255.192.0.0 / Router(config-if)#no shutdown / %LINK-5-CHANGED: Interface FastEthernet0/0, changed state to up / %LINEPROTO-5-UPDOWN: Line protocol on Interface FastEthernet0/0, changed state to up / Router(config-if)#exit / Router(config)#inter / Router(config)#interface Fa / Router(config)#interface FastEthernet 0/1 / Router(config-if)#ip address 11.128.0.1 255.192.0.0 / Router(config-if)#no shutdown / %LINK-5-CHANGED: Interface FastEthernet0/1, changed state to up / %LINEPROTO-5-UPDOWN: Line protocol on Interface FastEthernet0/1, changed state to up / Router(config-if)#exit / Router(config)#inter / Router(config)#interface Se / Router(config)#interface Serial 0/0/0 / Router(config-if)#ip address 192.168.2.2 255.255.255.252 / Router(config-if)#no shutdown / Router(config-if)# / %LINK-5-CHANGED: Interface Serial0/0/0, changed state to up / %LINEPROTO-5-UPDOWN: Line protocol on Interface Serial0/0/0, changed state to up / Router(config-if)#exit / Router(config)#inter / Router(config)#interface Se / Router(config)#interface Serial 0/0/1 / Router(config-if)#ip address 192.168.1.2 255.255.255.252 / Router(config-if)#no shutdown / %LINK-5-CHANGED: Interface Serial0/0/1, changed state to up / %LINEPROTO-5-UPDOWN: Line protocol on Interface Serial0/0/1, changed state to up
Router 2	FastEthernet 0/0	200.15.192.0 / 255.255.192.0
Router 2	FastEthernet 0/1	200.15.64.0 / 255.255.192.0
Router 2	Serial 0/0/0	192.168.1.1 / 255.255.255.252
Router>enable / Router#configure terminal / Enter configuration commands, one per line. End with CNTL/Z. / Router(config)#inter / Router(config)#interface Fa / Router(config)#interface FastEthernet 0/0 / Router(config-if)#ip address 200.15.192.1 255.255.192.0 / Router(config-if)#no shutdown / %LINK-5-CHANGED: Interface FastEthernet0/0, changed state to up / %LINEPROTO-5-UPDOWN: Line protocol on Interface FastEthernet0/0, changed state to up / Router(config-if)#exit / Router(config)#interface Fa / Router(config)#interface FastEthernet 0/1 / Router(config-if)#ip address 200.15.64.1 255.255.192.0 / Router(config-if)#no shutdown / %LINK-5-CHANGED: Interface FastEthernet0/1, changed state to up / %LINEPROTO-5-UPDOWN: Line protocol on Interface FastEthernet0/1, changed state to up / Router(config-if)#exit / Router(config)#inter / Router(config)#interface Se / Router(config)#interface Serial 0 / Router(config)#interface Serial 0/0/0 / Router(config-if)#ip address 192.168.1.1 255.255.255.252 / Router(config-if)#no shutdown / %LINK-5-CHANGED: Interface Serial0/0/0, changed state to up / %LINEPROTO-5-UPDOWN: Line protocol on Interface Serial0/0/0, changed state to up

- Configureu el servei DHCP per a les xarxes LAN
Router0 - FastEthernet0/0 / Router>enable / Router#conf / Router#configure ter / Router#configure terminal / Enter configuration commands, one per line. End with CNTL/Z. / Router(config)#service dhcp / Router(config)#ip dhcp pool POOL1 / Router(dhcp-config)#network 163.27.180.0 255.255.240.0 / Router(dhcp-config)#default-router 163.27.180.1 / Router(dhcp-config)#ip dhcp excluded-address 163.27.180.1 / Router(config)#exit / Router# / %SYS-5-CONFIG_I: Configured from console by console / Router0 - FastEthernet0/1 / Router>enable / Router#conf / Router#configure ter / Router#configure terminal / Enter configuration commands, one per line. End with CNTL/Z. / Router(config)#service dhcp / Router(config)#ip dhcp pool POOL2 / Router(dhcp-config)#network 163.27.240.0 255.255.240.0 / Router(dhcp-config)#default-router 163.27.240.1 / Router(dhcp-config)#ip dhcp excluded-address 163.27.240.1 / Router(config)#exit / Router# / %SYS-5-CONFIG_I: Configured from console by console / Router1 - FastEthernet0/0 / Router>enable / Router#conf / Router#configure / Configuring from terminal, memory, or network [terminal]? / Enter configuration commands, one per line. End with CNTL/Z. / Router(config)#service dhcp / Router(config)#ip dhcp pool POOL3 / Router(dhcp-config)#network 11.192.0.0 255.192.0.0 / Router(dhcp-config)#default-router 11.192.0.1 / Router(dhcp-config)#ip dhcp excluded-address 11.192.0.1 / Router(config)#exit / Router# / %SYS-5-CONFIG_I: Configured from console by console / Router1 - FastEthernet0/1 / Router#configure ter / Router#configure terminal / Enter configuration commands, one per line. End with CNTL/Z. / Router(config)#ip dhcp pool POOL4 / Router(dhcp-config)#network 11.128.0.0 255.192.0.0 / Router(dhcp-config)#default-router 11.128.0.1 / Router(dhcp-config)#ip dhcp excluded-address 11.128.0.1 / Router(config)#exit / Router# / %SYS-5-CONFIG_I: Configured from console by console / Router2 - FastEthernet0/0 / Router>enable / Router#configure ter / Router#configure terminal / Enter configuration commands, one per line. End with CNTL/Z. / Router(config)#service dhcp / Router(config)#ip dhcp pool POOL5 / Router(dhcp-config)#network 200.15.192.0 255.255.192.0 / Router(dhcp-config)#default-router 200.15.192.1 / Router(dhcp-config)#ip dhcp excluded-address 200.15.192.1 / Router(config)#exit / Router# / %SYS-5-CONFIG_I: Configured from console by console / Router2 - FastEthernet0/1 / Router#configure ter / Router#configure terminal / Enter configuration commands, one per line. End with CNTL/Z. / Router(config)#ip dhcp pool POOL6 / Router(dhcp-config)#network 200.15.64.0 255.255.192.0 / Router(dhcp-config)#default-router 200.15.64.1 / Router(dhcp-config)#ip dhcp excluded-address 200.15.64.1 / Router(config)#exit / Router# / %SYS-5-CONFIG_I: Configured from console by console / Router#

- Configureu l'enrutament dinàmic amb RIP de forma que no envïi actualitzacions a les LAN finals
passive-interface FasthEthernet 0/0 / passive-interface FastEthernet0/1 / Així a les 3 xarxes connectats als routers

Utilitzeu primer RIPv1, i després, RIPv2
Router0 / Router>enable / Router#configure terminal / Router#debug ip rip / RIP protocol debugging is on / Router#configure terminal / Enter configuration commands, one per line. End with CNTL/Z. / Router(config)#router rip / Router(config-router)#network 11.192.0.0 / Router(config-router)#network 11.128.0.0 / Router(config-router)#network 200.15.192.0 / Router(config-router)#network 200.15.64.0 / Router(config)#exit / Router# / %SYS-5-CONFIG_I: Configured from console by console / Router#show ip rip database / Router#show ip route / Codes: C - connected, S - static, I - IGRP, R - RIP, M - mobile, B - BGP / D - EIGRP, EX - EIGRP external, O - OSPF, IA - OSPF inter area / N1 - OSPF NSSA external type 1, N2 - OSPF NSSA external type 2 / E1 - OSPF external type 1, E2 - OSPF external type 2, E - EGP / i - IS-IS, L1 - IS-IS level-1, L2 - IS-IS level-2, ia - IS-IS inter area / * - candidate default, U - per-user static route, o - ODR / P - periodic downloaded static route / Gateway of last resort is not set / 163.27.0.0/20 is subnetted, 2 subnets / C 163.27.176.0 is directly connected, FastEthernet0/0 / C 163.27.240.0 is directly connected, FastEthernet0/1 / 192.168.2.0/30 is subnetted, 1 subnets / C 192.168.2.0 is directly connected, Serial0/0/0 / Router#show ip protocol / Routing Protocol is "rip" / Sending updates every 30 seconds, next due in 5 seconds / Invalid after 180 seconds, hold down 180, flushed after 240 / Outgoing update filter list for all interfaces is not set / Incoming update filter list for all interfaces is not set / Redistributing: rip / Default version control: send version 1, receive any version / Interface Send Recv Triggered RIP Key-chain / Automatic network summarization is in effect / Maximum path: 4 / Routing for Networks: / 11.0.0.0 / 200.15.64.0 / 200.15.192.0 / Passive Interface(s): / FastEthernet0/0 / FastEthernet0/1 / Routing Information Sources: / Gateway Distance Last Update / Distance: (default is 120) / Router# / ROUTER0 V2 RIP / Router# / %SYS-5-CONFIG_I: Configured from console by console / Router#debug ip rip / RIP protocol debugging is on / Router#conf / Router#configure ter / Router#configure terminal / Enter configuration commands, one per line. End with CNTL/Z. / Router(config)# / Router(config)#router rip / Router(config-router)#version 2 / Router(config-router)#network 11.192.0.0 / Router(config-router)#network 11.128.0.0 / Router(config-router)#network 200.15.192.0 / Router(config-router)#network 200.15.64.0 / Router(config-router)#no auto-s / Router(config-router)#no auto-summary / Router(config-router)#end / Router# / %SYS-5-CONFIG_I: Configured from console by console / Router# / Router1 / Router>enable / Router#debug ip rip / RIP protocol debugging is on / Router#configure ter / Router#configure terminal / Enter configuration commands, one per line. End with CNTL/Z. / Router(config)#router rip / Router(config-router)#network 163.27.180.0 / Router(config-router)#network 163.27.240.0 / Router(config-router)#network 200.15.192.0 / Router(config-router)#network 200.15.64.0 / Router(config-router)#exit / Router(config)#exit / Router# / %SYS-5-CONFIG_I: Configured from console by console / Router#show ip rip database / Router#show ip route / Codes: C - connected, S - static, I - IGRP, R - RIP, M - mobile, B - BGP / D - EIGRP, EX - EIGRP external, O - OSPF, IA - OSPF inter area / N1 - OSPF NSSA external type 1, N2 - OSPF NSSA external type 2 / E1 - OSPF external type 1, E2 - OSPF external type 2, E - EGP / i - IS-IS, L1 - IS-IS level-1, L2 - IS-IS level-2, ia - IS-IS inter area / * - candidate default, U - per-user static route, o - ODR / P - periodic downloaded static route / Gateway of last resort is not set / 11.0.0.0/10 is subnetted, 2 subnets / C 11.128.0.0 is directly connected, FastEthernet0/1 / C 11.192.0.0 is directly connected, FastEthernet0/0 / 192.168.1.0/30 is subnetted, 1 subnets / C 192.168.1.0 is directly connected, Serial0/0/1 / 192.168.2.0/30 is subnetted, 1 subnets / C 192.168.2.0 is directly connected, Serial0/0/0 / Router#show ip protocol / Routing Protocol is "rip" / Sending updates every 30 seconds, next due in 4 seconds / Invalid after 180 seconds, hold down 180, flushed after 240 / Outgoing update filter list for all interfaces is not set / Incoming update filter list for all interfaces is not set / Redistributing: rip / Default version control: send version 1, receive any version / Interface Send Recv Triggered RIP Key-chain / Automatic network summarization is in effect / Maximum path: 4 / Routing for Networks: / 163.27.0.0 / 200.15.64.0 / 200.15.192.0 / Passive Interface(s): / FastEthernet0/0 / FastEthernet0/1 / Routing Information Sources: / Gateway Distance Last Update / Distance: (default is 120) / Router# / ROUTER1 V2 RIP / Router# / %SYS-5-CONFIG_I: Configured from console by console / debug / % Incomplete command. / Router#debug ip rip / RIP protocol debugging is on / Router#conf / Router#configure ter / Router#configure terminal / Enter configuration commands, one per line. End with CNTL/Z. / Router(config)#router rip / Router(config-router)#version 2 / Router(config-router)#network 163.27.180.0 / Router(config-router)#network 163.27.240.0 / Router(config-router)#network 200.15.192.0 / Router(config-router)#network 200.15.64.0 / Router(config-router)#no auto-s / Router(config-router)#no auto-summary / Router(config-router)#end / Router# / %SYS-5-CONFIG_I: Configured from console by console / Router# / Router2 / Router>enable / Router#debug ip rip / RIP protocol debugging is on / Router#conf / Router#configure ter / Router#configure terminal / Enter configuration commands, one per line. End with CNTL/Z. / Router(config)#router rip / Router(config-router)#network 11.128.0.0 / Router(config-router)#network 11.192.0.0 / Router(config-router)#network 163.27.180.0 / Router(config-router)#exit / Router(config)#exit / Router# / %SYS-5-CONFIG_I: Configured from console by console / Router#show ip rip database / Router#show ip route / Codes: C - connected, S - static, I - IGRP, R - RIP, M - mobile, B - BGP / D - EIGRP, EX - EIGRP external, O - OSPF, IA - OSPF inter area / N1 - OSPF NSSA external type 1, N2 - OSPF NSSA external type 2 / E1 - OSPF external type 1, E2 - OSPF external type 2, E - EGP / i - IS-IS, L1 - IS-IS level-1, L2 - IS-IS level-2, ia - IS-IS inter area / * - candidate default, U - per-user static route, o - ODR / P - periodic downloaded static route / Gateway of last resort is not set / 192.168.1.0/30 is subnetted, 1 subnets / C 192.168.1.0 is directly connected, Serial0/0/0 / C 200.15.64.0/18 is directly connected, FastEthernet0/1 / C 200.15.192.0/18 is directly connected, FastEthernet0/0 / Router#show ip protocol / Routing Protocol is "rip" / Sending updates every 30 seconds, next due in 25 seconds / Invalid after 180 seconds, hold down 180, flushed after 240 / Outgoing update filter list for all interfaces is not set / Incoming update filter list for all interfaces is not set / Redistributing: rip / Default version control: send version 1, receive any version / Interface Send Recv Triggered RIP Key-chain / Automatic network summarization is in effect / Maximum path: 4 / Routing for Networks: / 11.0.0.0 / 163.27.0.0 / Passive Interface(s): / FastEthernet0/0 / FastEthernet0/1 / Routing Information Sources: / Gateway Distance Last Update / Distance: (default is 120) / Router# / ROUTER2 V2 RIP / Router# / %SYS-5-CONFIG_I: Configured from console by console / Router#debug ip rip / RIP protocol debugging is on / Router#conf / Router#configure ter / Router#configure terminal / Enter configuration commands, one per line. End with CNTL/Z. / Router(config)#router rip / Router(config-router)#version 2 / Router(config-router)#network 163.27.180.0 / Router(config-router)#network 163.27.240.0 / Router(config-router)#network 11.192.0.0 / Router(config-router)#network 11.128.0.0 / Router(config-router)#no auto / Router(config-router)#no auto-summary / Router(config-router)#end / Router# / %SYS-5-CONFIG_I: Configured from console by console / Router#

Responeu a les següents preguntes:
Enganxa les línies que has utilitzat per configurar el servei DHCP al Router0
Router0 - FastEthernet0/0 / Router>enable / Router#conf / Router#configure ter / Router#configure terminal / Enter configuration commands, one per line. End with CNTL/Z. / Router(config)#service dhcp / Router(config)#ip dhcp pool POOL1 / Router(dhcp-config)#network 163.27.180.0 255.255.240.0 / Router(dhcp-config)#default-router 163.27.180.1 / Router(dhcp-config)#ip dhcp excluded-address 163.27.180.1 / Router(config)#exit / Router# / %SYS-5-CONFIG_I: Configured from console by console / Router0 - FastEthernet0/1 / Router>enable / Router#conf / Router#configure ter / Router#configure terminal / Enter configuration commands, one per line. End with CNTL/Z. / Router(config)#service dhcp / Router(config)#ip dhcp pool POOL2 / Router(dhcp-config)#network 163.27.240.0 255.255.240.0 / Router(dhcp-config)#default-router 163.27.240.1 / Router(dhcp-config)#ip dhcp excluded-address 163.27.240.1 / Router(config)#exit / Router# / %SYS-5-CONFIG_I: Configured from console by console

1. Quina instrucció has utilitzat per no enviar actualitzacions a les LAN finals?
Router⦿(config-router)# passive-interface Interfı́cie_local

1. Enganxa les taules d'enrutament dels 3 routers per RIPv1
Router0 / Router#show ip route / Codes: C - connected, S - static, I - IGRP, R - RIP, M - mobile, B - BGP / D - EIGRP, EX - EIGRP external, O - OSPF, IA - OSPF inter area / N1 - OSPF NSSA external type 1, N2 - OSPF NSSA external type 2 / E1 - OSPF external type 1, E2 - OSPF external type 2, E - EGP / i - IS-IS, L1 - IS-IS level-1, L2 - IS-IS level-2, ia - IS-IS inter area / * - candidate default, U - per-user static route, o - ODR / P - periodic downloaded static route / Gateway of last resort is not set / 163.27.0.0/20 is subnetted, 2 subnets / C 163.27.176.0 is directly connected, FastEthernet0/0 / C 163.27.240.0 is directly connected, FastEthernet0/1 / 192.168.2.0/30 is subnetted, 1 subnets / C 192.168.2.0 is directly connected, Serial0/0/0 / Router# / Router1 / Router#show ip route / Codes: C - connected, S - static, I - IGRP, R - RIP, M - mobile, B - BGP / D - EIGRP, EX - EIGRP external, O - OSPF, IA - OSPF inter area / N1 - OSPF NSSA external type 1, N2 - OSPF NSSA external type 2 / E1 - OSPF external type 1, E2 - OSPF external type 2, E - EGP / i - IS-IS, L1 - IS-IS level-1, L2 - IS-IS level-2, ia - IS-IS inter area / * - candidate default, U - per-user static route, o - ODR / P - periodic downloaded static route / Gateway of last resort is not set / 11.0.0.0/10 is subnetted, 2 subnets / C 11.128.0.0 is directly connected, FastEthernet0/1 / C 11.192.0.0 is directly connected, FastEthernet0/0 / 192.168.1.0/30 is subnetted, 1 subnets / C 192.168.1.0 is directly connected, Serial0/0/1 / 192.168.2.0/30 is subnetted, 1 subnets / C 192.168.2.0 is directly connected, Serial0/0/0 / Router# / Router2 / Router#show ip route / Codes: C - connected, S - static, I - IGRP, R - RIP, M - mobile, B - BGP / D - EIGRP, EX - EIGRP external, O - OSPF, IA - OSPF inter area / N1 - OSPF NSSA external type 1, N2 - OSPF NSSA external type 2 / E1 - OSPF external type 1, E2 - OSPF external type 2, E - EGP / i - IS-IS, L1 - IS-IS level-1, L2 - IS-IS level-2, ia - IS-IS inter area / * - candidate default, U - per-user static route, o - ODR / P - periodic downloaded static route / Gateway of last resort is not set / 192.168.1.0/30 is subnetted, 1 subnets / C 192.168.1.0 is directly connected, Serial0/0/0 / C 200.15.64.0/18 is directly connected, FastEthernet0/1 / C 200.15.192.0/18 is directly connected, FastEthernet0/0 / Router#

1. Enganxa les bases de dades d'enrutament dinàmic dells 3 routers per RIPv1
Router0 / Router>enable / Router#show ip rip database / 163.27.176.0/20 auto-summary / 163.27.176.0/20 directly connected, FastEthernet0/0 / 163.27.240.0/20 auto-summary / 163.27.240.0/20 directly connected, FastEthernet0/1 / Router1 / Router#show ip rip database / 11.128.0.0/10 auto-summary / 11.128.0.0/10 directly connected, FastEthernet0/1 / 11.192.0.0/10 auto-summary / 11.192.0.0/10 directly connected, FastEthernet0/0 / Router2 / Router#show ip rip database / 200.15.64.0/18 auto-summary / 200.15.64.0/18 directly connected, FastEthernet0/1 / 200.15.192.0/18 auto-summary / 200.15.192.0/18 directly connected, FastEthernet0/0 / Router#

1. Enganxa les taules d'enrutament dels 3 routers per RIPv2
Router0 / Router#show ip protocol / Routing Protocol is "rip" / Sending updates every 30 seconds, next due in 22 seconds / Invalid after 180 seconds, hold down 180, flushed after 240 / Outgoing update filter list for all interfaces is not set / Incoming update filter list for all interfaces is not set / Redistributing: rip / Default version control: send version 2, receive 2 / Interface Send Recv Triggered RIP Key-chain / Automatic network summarization is not in effect / Maximum path: 4 / Routing for Networks: / 11.0.0.0 / 163.27.0.0 / 200.15.64.0 / 200.15.192.0 / Passive Interface(s): / FastEthernet0/0 / FastEthernet0/1 / Routing Information Sources: / Gateway Distance Last Update / Distance: (default is 120) / Router1 / Router#show ip protocol / Routing Protocol is "rip" / Sending updates every 30 seconds, next due in 22 seconds / Invalid after 180 seconds, hold down 180, flushed after 240 / Outgoing update filter list for all interfaces is not set / Incoming update filter list for all interfaces is not set / Redistributing: rip / Default version control: send version 2, receive 2 / Interface Send Recv Triggered RIP Key-chain / Automatic network summarization is not in effect / Maximum path: 4 / Routing for Networks: / 11.0.0.0 / 163.27.0.0 / 200.15.64.0 / 200.15.192.0 / Passive Interface(s): / FastEthernet0/0 / FastEthernet0/1 / Routing Information Sources: / Gateway Distance Last Update / Distance: (default is 120) / Router2 / Router#show ip protocol / Routing Protocol is "rip" / Sending updates every 30 seconds, next due in 0 seconds / Invalid after 180 seconds, hold down 180, flushed after 240 / Outgoing update filter list for all interfaces is not set / Incoming update filter list for all interfaces is not set / Redistributing: rip / Default version control: send version 2, receive 2 / Interface Send Recv Triggered RIP Key-chain / Automatic network summarization is not in effect / Maximum path: 4 / Routing for Networks: / 11.0.0.0 / 163.27.0.0 / 200.15.64.0 / 200.15.192.0 / Passive Interface(s): / FastEthernet0/0 / FastEthernet0/1 / Routing Information Sources: / Gateway Distance Last Update / Distance: (default is 120) / Router#

Enganxa les bases de dades d'enrutament dinàmic dells 3 routers per RIPv2
Router0 / Router>enable / Router#show ip rip database / 163.27.176.0/20 auto-summary / 163.27.176.0/20 directly connected, FastEthernet0/0 / 163.27.240.0/20 auto-summary / 163.27.240.0/20 directly connected, FastEthernet0/1 / Router1 / Router#show ip rip database / 11.128.0.0/10 auto-summary / 11.128.0.0/10 directly connected, FastEthernet0/1 / 11.192.0.0/10 auto-summary / 11.192.0.0/10 directly connected, FastEthernet0/0 / Router2 / Router#show ip rip database / 200.15.64.0/18 auto-summary / 200.15.64.0/18 directly connected, FastEthernet0/1 / 200.15.192.0/18 auto-summary / 200.15.192.0/18 directly connected, FastEthernet0/0 / Router#

1. Quina és la diferència principal entre RIPv1 i RIPv2? Demostra aquesta diferència a través d'un exemple de les taules d'enrutament.
RIPv1:La versión 1 del protocolo de enrutamiento RIP es “con clase”, es decir que no soporta subredes, VLSM ni CIDR, no posee mecanismos de autenticación y no realiza actualizaciones desencadenadas por eventos. Todas estas limitaciones hicieron que con el paso del tiempo y las nuevas necesidades cayera en desuso. / Protocolo de enrutamiento Classful / Basado en el algoritmo Bellman-Ford / Redes de tamaño moderado / Basado en el protocolo UDP. Usa el puerto 250 / RIPv2:La versión 2 del protocolo de enrutamiento RIP es “sin clase”, soporta subredes, VLSM, CIDR, resumen de rutas, posee mecanismos de autenticación mediante texto plano o codificación MD5, realiza actualizaciones desencadenadas por eventos. / 15 saltos / Mecanismo de autenticación / Basado en algoritmo Bellmand-Ford / Redes de tamaño pequeño / Protocol de enrutamiento Classless( Admite VLSM)